## Slide 1
  Smart Irrigation
  By
  Team Name: Amigos
  TEAM MEMBERS:
  1.MOHAMMED ASRA FATIMA
  Email: fatima07asra@gmail.com
  Contact no: 9515307883
  2.SABRINA SHAIK
  Email: sabrina.shaik80@gmail.com
  Contact no: 9642550879
  3.SAMREEN BEGUM
  Email: samreen15102000@gmail.com
  Contact no: 6301 017 251
  4.MOHAMMED IMAZ AHSAN
  Email:imaz913126@gmail.com
  Contact no:7702982829

## Slide 5: Smart Irrigation
Introduction:
Agriculture is the unquestionably the largest livelihood provider in India. With rising population, there is a need for increased agricultural production. In order to support greater production in farms, the requirement of the amount of fresh water used in irrigation also rises.
We tend to propose a solution of developing an automated irrigation system using IoT that could be controlled through mobile application.
Idea Explanation:
Our IoT based application will work to minimize the number of workers in a crop field, control and save water and electricity, Increase agricultural production using small quantities of water, minimize manual intervention in watering operations with increasing watering speed and preserving plants from fungi.

## Slide 6: Block Diagram
YL69 Soil Moisture Sensor
LM35
Temperature Sensor
DHT11
Humidity Sensor
Relay
Power Supply
Arduino Micro Controller
Motor
Mobile Device
GSM GPRS SIM900A modem
Acoustic Sensor

## Slide 7: Hardware Components Required
Arduino Micro Controller
YL69 Soil Moisture Sensor
LM35 Temperature Sensor
DHT11 Humidity Sensor
Acoustic sensor
Relay
GSM GPRS SIM900A modem
Rechargeable battery for Power Supply
Pump
1.
2.
3.
4.
7.
8.
5.

## Slide 8
Hardware circuit setup

## Slide 9
Complete circuit diagram
12V DC,1Amp POWER SOURCE
Channel Relay Module Board 5V LOW level trigger
12 V DC MOTOR WATER PUMP
Soil moisture
sensor
Material | Features
Arduino | Microcontroller AT mega328 Voltage of operating 5V Recommended input voltage 7-9V Range of input voltage 6-20V
Moisture sensor | Voltage of working 5v Current of working ˂ 20 mA Analog interface Detection depth 37mm Working temperature range 10 ͦC-30 Cͦ
Water pump | Voltage of Input: 6-12 VDC Rate of Flow: 1.5-2 L/min Temperature of Operation: 80 ͦ C Current of Operating: 0.5-0.7A Distance of Suction: 2 meter (Max) Pump Life: 2500 Hour
Rechargeable Battery | Type Lead acid Battery. Model PP 2.3-12 SV code 380301 AALV4 Brand Power Plus Color Black Battery Voltage 12V

## Slide 10: Software Programming techniques
The following IBM Watson Services are used
Node-RED: Node-RED is used to build a effective and user friendly user interface, IBM iot new-in node is used to fetch the input values from the Watson stimulators.
IBM IoT platform to create a virtual device connected with the Watson stimulators and configured with the node red flow.
Watson IoT Stimulators work as the sensors which give output values in JSON format.
JSON Format: JavaScript Object Notation or JSON is an open-standard file format that uses human-readable text to transmit data objects consisting of attribute– value pairs and array data types (or any other serializable value).

## Slide 11: Application View
Smart Irrigation
Temperature
Humidity
Soil Moisture
Motor Status
OFF
ON
Readings
Click here for Graph
Home page
Sensor readings
Humidity Graph
Crop type 1
Crop type 2
Back
21.23F
61.39%
12%
Pests Map

## Slide 12
On clicking
On clicking
On clicking
Pests Map
on Sensor readings page
on Sensor readings page
on Sensor readings page
On clicking
on Sensor readings page

## Slide 13
Flow chart of Temperature/Humidity Sensor
Process implementation
Soil moisture sensor
System working

## Slide 14
Smart Irrigation application currently provides 3 features
1. Monitoring of soil moisture, humidity & temperature for better understand with a graph output
2. Provides motor switch connected with the hardware motor pump to irrigate the field on a single tab by the farmer.
3. Detects the pests present near any crop & Provides a top view map of the field indicting vulnerable crop areas of the field affected by pests.The end user of the smart irrigation app will be a farmer.

## Slide 15
Animated representation of Smart Irrigation

## Slide 16
Thank you